## Slide 1: BASIC ULTRASOUND PHYSICS
KATHIRVEL SUBRAMANIAM MD MPH

## Slide 2: Question 1
Increasing frequency of the transducer does all except
Improves axial resolution
Decreases wavelength
Decreases depth of penetration
Increases pulse length

## Slide 3: Q 2
Propagation speed is
Determined by the density and stiffness of the medium
Determined by the source
Is 1540 m/sec in the cardiac tissue
Is 1540 km/sec in cardiac tissue

## Slide 4: Q3
Temporal resolution can be improved by
Using single focus
Using narrow sector
Minimizing line density
Maximizing depth of view

## Slide 5: Q4
When the angle between the sound beam and direction of motion is 90 degrees, the measured velocity is equal to
True velocity
0
20% true velocity
Peak velocity

## Slide 6: Q5
In phased array transducer, beam steering and focusing is achieved by
Manually rotating the transducer
Mechanically rotating transducer
Changing resonant frequency of piezo electric crystals
Changing the timing of pulses to the piezo electric elements

## Slide 7: SOUND WAVES

## Slide 8: SOUND WAVES
LONGITUDINAL WAVE

## Slide 9: SOUND WAVES

## Slide 10: SOUND WAVES
LONGITUDINAL WAVES
COMPRESSION AND RAREFACTION
CHARACTERS (FREQUENCY, PERIOD, AMPLITUDE, WAVELENGTH, VELOCITY)

## Slide 11: FREQUENCY
HUMAN EARS CAN HEAR 20 Hz to 20 KHz
FREQUENCY ABOVE 20 KHz IS CALLED ULTRASOUND
DIAGNOSTIC ULTRASOUND USED 1-20 MHz

## Slide 12: VELOCITY
PROPAGATION VELOCITY
FASTEST IN BONE 3000 m/sec
SLOWEST IN LUNGS 700 m/sec
HEART, BLOOD , BLOOD VESSELS, SOFT TISSUE – 1540 m/sec

## Slide 13: WAVELENGTH
WAVELENGTH = VELOCITY/FREQUENCY
= 1540 m/sec /5 MHz
= 1.54/5
= 0.308 mm

## Slide 14: WAVELENGTH VS FREQUENCY
WAVELENGTH AND FREQUENCY INVERSELY RELATED
INCREASED WAVELENGTH OR DECREASE IN FREQUENCY WILL CAUSE DECREASED RESOLUTION OF AN IMAGE
BUT IMPROVE PENETRATION OF A SOUND WAVE TO IMAGE DEEPER STRUCTURES

## Slide 15: PENETRATION VS RESOLUTION

## Slide 16: Amplitude, Power and Intensity
Energy or acoustic pressure of an ultrasound signal
Described in Decibels
Echo-image 1-120 Decibels
Increased energy Power related to bio-effects (Temperature elevation and cavitation)

## Slide 17: ULTRASOUND TISSUE INTERACTION
STIFFNESS
DENSITY
THEIR RELATION TO PROPAGATION SPEED (STIFFNESS IS DIRECTLY RELATED TO SPEED- BONE MOST STIFF)
ACOUSTIC IMPEDENCE = DENSITY MULTIPLIED BY PROPAGATION SPEED, DETERMINES THE ULTRASOUND TRANSMISSION AND REFLECTION AT TISSUE BOUNDARIES

## Slide 18: US TISSUE INTERACTIONS

## Slide 19: REFLECTION
RESPONSIBLE FOR IMAGE FORMATION
DEPENDS ON TWO FACTORS ACOUSTIC IMPEDENCE AND ANGLE OF REFLECTION
ULTRASOUND DROP OUTS RESULTS FROM PARALLEL ALIGNMENT BETWEEN TISSUE INTERFACE AND ULTRASOUND BEAM

## Slide 21: SCATTERING
OCCURS IN MOVING BLOOD ELEMENTS SUCH AS RED BLOOD CELLS
RED CELLS ARE SMALLER IN SIZE THAN WAVELENGTH BASIS FOR SCATTERING
BASIS FOR DOPPLER ECHOCARDIOGRAPHY
SCATTERING AT TISSUES BASIS FOR TISSUE DOPPLER AND SPECKLE IMAGING

## Slide 22: REFRACTION
OCCURS WHEN DEFLECTION OF SOUND WAVE OCCURS AS THEY PASS THROUGH MEDIUM WITH DIFFERENT ACOUSTIC IMPEDENCE
LENS IN FRONT OF THE TRANSDUCER USED TO FOCUS PRODUCES PLANNED REFRACTION
UNPLANNED REFRACTION RESPONSIBLE FOR ARTIFACTS OR DOUBLE IMAGES

## Slide 23: ATTENUATION
ATTENUATION DETERMINES PENETRATION DEPTH
FREQUENCY AND WAVELENGTH RELATED
1 MHz probe – US PENETRATION DEPTH 30 cm 5MHz probe - US PENETRATION DEPTH 6 CM

## Slide 24: TRANSDUCER

## Slide 25: COMPONENTS
PIEZO ELECTRIC CRYSTAL (LEAD ZIRCONATE TITANATE)
CRYSTALS COMPRESS AND EXPAND
TRANSMITTER AND RECEIVER FUNCTIONS
BACKING OR DAMPING MATERIAL (REDUCES RINGING OF CRYSTALS TO PRODUCE SHORT PULSE LENGTH TO IMPROVE SPATIAL RESOLUTION)
MATCHING LAYER- IMPROVES TRANSMISSION OF US BETWEEN PZT AND TISSUE SURFACE
LENS- FOCUS

## Slide 26: TYPES OF TRANSDUCERS
LINEAR ARRAY (7-12 MHz); VASCULAR ACCESS
PHASED ARRAY (2-4 MHz); CARDIAC
CURVILINEAR ARRAY (2-6 MHz); ABDOMINAL

## Slide 28: PULSED ULTRASOUND

## Slide 29: DIAGNOSTIC ULTRASOUND
PULSED ULTRASOUND
PULSE DURATION, PULSE LENGTH
PULSE REPITION PERIOD AND PULSE REPITION FREQUENCY
DUTY FACTOR = PULSE DURATION / PRP X 100
1% 2D ECHO, 5% PWD AND 100% CWD

## Slide 30: RESOLUTION
SPATIAL (AXIAL, LATERAL AND ELEVATIONAL)
TEMPORAL

## Slide 31: AXIAL RESOLUTION
DEPENDS ON
SPATIAL PULSE LENGTH

## Slide 32: IMAGE RESOLUTION

## Slide 33: LATERAL AND ELEVATIONAL RESOLUTION
BEAM WIDTH (FOCUS) AT EACH DEPTH IS THE MAJOR DETERMINANT

## Slide 34: FOCAL ZONE
NEAR ZONE
FOCAL ZONE
FAR ZONE

## Slide 35: FOCAL ZONE

## Slide 36: LATERAL RESOLUTION

## Slide 37: TEMPORAL RESOLUTION
FRAME RATE- FRAMES PER SECOND
INCREASED FRAME RATE- INCREASED ABILITY TO APPRECIATE RAPIDLY CHANGING EVENTS
HIGHER FRAME RATE HIGHER TEMPORAL RESOLUTION

## Slide 38: TEMPORAL RESOLUTION

## Slide 39: TEMPORAL RESOLUTION

## Slide 40: ULTRASOUND MODALITIES
TWO DIMENSIONAL ECHOCARDIOGRAPHY
M MODE
THREE DIMENSIONAL ECHOCARDIOGRAPHY
DOPPLER ECHOCARDIOGRAPHY (COLOR AND SPECTRAL DOPPLER) SPECTRAL- PULSE WAVE AND CONTINUOUS WAVE

## Slide 41: M -MODE
MOTION MODE
MOTION VERSUS TIME AND DEPTH
HIGH SAMPLING RATE AND TEMPORAL RESOLUTION
USED TO EVALUATE RAPIDLY MOVING STRUCTURES

## Slide 42: M-MODE LV

## Slide 43: M MODE AV

## Slide 44: Doppler Principle
Change in frequency of transmitted ultrasound signal by backscattering from small moving structures such as Red blood cells intercepted by the ultrasound beam
Frequency shift is higher if the red cells are moving towards the transducer (Positive doppler effect)
Frequency shift is lower if the red cells are moving away from the transducer (Negative Doppler effect)
Doppler ultrasound is audible ( 0-20 KHz)

## Slide 45: Doppler effect

## Slide 46: Doppler equation
Blood flow Velocity from Doppler equation
= c (FS-FT)/ 2FT (Cosθ)
C = Speed of sound
Fs= Scattered frequency
Ft= Transmitted frequency
Θ= Angle between blood flow and ultrasound beam

## Slide 47: Spectral analysis
Backscattering contains multiple frequencies
Analysis of frequencies done FFT
Direction, velocity and amplitude

## Slide 48: CW Doppler
All velocities in the path analyzed
FULL envelope
High velocities analyzed
Range Ambiguity; Inability to locate the site of high velocity
No Aliasing

## Slide 49: Pulse wave Doppler
Only the velocity in the selected location is analyzed
HOLLOW Appearance
No Range ambiguity
Susceptible to aliasing
Not the Doppler modality to analyze the highest velocity

## Slide 50: Nyquist limit
Maximum detectable frequency shift
If velocity exceeds, cuts above baseline at the top
Use CWD
Shift baseline
Low frequency transducer
High PRF Doppler, Increase PRF for the depth (NL= PRF/2)

## Slide 51: COLOR FLOW DOPPLER
Pulse wave Doppler
Multiple scan lines and multiple gates of sampling
Frame rate and temporal resolution are important issues with CFD!
Direction of flow, Magnitude and quality of flow

## Slide 52: Velocity map versus Variance map

## Slide 53: Laminar vs Turbulence